## Slide 1: OpenDaylight: Service Function Chaining

## Slide 2: Topics
What is Service Chaining?
Service Chaining “Components”
ODL and Service Chaining
Complementary Projects

## Slide 3: Network Service Insertion Today
Network services are ubiquitous
  Firewall and load balancer are in almost every data center
Current state of the art is topology dependent
  Very complex: VLAN-stitching, Policy Based Routing (PBR), etc.
  Static: no dynamic, horizontal or vertical scaling, requires network changes
Service chaining is accomplished via hop-by-hop switching/routing changes
No way to share valuable information between the network and services, or between service functions

## Slide 4: Service Chaining
Service chaining is the broad term that describes delivering multiple service functions in a specific order
  Decouples network topology and service functions
  Supports dynamic insertion of service functions
  Common model for all types of services
  Enables the sharing of information between service functions
Composed of data plane and control/policy planes
  Overlay data plane Control and policy planes
IETF WG: Service Function Chaining (SFC)
  https://datatracker.ietf.org/wg/sfc/

## Slide 5: Service Chaining: Service Graphs
Sub-graphs define service chains from the overall service graph
Service functions can be in more than one chain
A service path is the specific instantiation of a service chain
  Chain1: S1S2S6S8
  Pathn: instance(S1)  instance(S2)  instance(S6)  instance (S8)

## Slide 6: Service Chaining Components
Classifier: determines what traffic needs to be chained based on policy.
Service Chain: the intended set of service that must be traversed.
Service Path: the actual instances of services traversed.
Service Overlay: topology created to realize a service path.
Metadata: information passed between participating nodes.

## Slide 7: ODL and Service Chaining

## Slide 8: Service Chaining Service
Receives information about chain and/or path to be constructed via northbound API
Information about available service nodes are contained in the node datastore
Constructs service path:
  Simple: just a list
  Complex: constrained list (e.g. bandwidth, capabilities, etc.)

## Slide 9: Example SC Application
Presents list of available services (types and other instances) to the end user
Southbound RESTCONF to ODL
  List of service type  chain
  List of service function  path
Can evolve to pass constraints as well (not in current scope)

## Slide 10: Plugins
Support several south-bound protocols
  NC/YANG
  LISP
  Openflow
Register service function and present them to the node datastore
Pass metadata to participating nodes
Create the needed topology
  Evolve from simple static end-points to dynamic mapping (see LISP service)

## Slide 11: Complementary Projects
LISP Service
  LISP can provide the needed overlay to create a service path
  Use LISP API to “map” service locators
Group Based Policy
  Service chains are instantiations of policy
  Service chains are part of a contract
  Policy metadata passed along service chain